# Vector Video
## 1. Introduction
The vector video card is an easy way to display an image on an X-Y oscilloscope display.
The card supports beam blanking and by default has a 128x128 point cloud resolution. It is designed to work with the Pandora X16 computer bus. The system can be reconfigured to use additional memory to increase the point cloud resolution up to 32,767.
## 2. Digital setup
  1. Display modes
The card can be configured in different display modes depending on the desired resolution. The mode of operation is set at address h0000 of the card. The bits of address h0000 are laid out like this:
0	1	2	3	4	5	6	7
M0	M1	M2	M3	DRW	ST0	ST1	-

- M0..M3: Define the mode the display is operating in, M2 to M3 are currently unused.
- DRW: Indicates if the card is currently drawing. This bit cannot be written to.
- ST0..ST1: Indicates the status of the card. These bits may denote errors. These bits cannot be written to.
- - : Unused.

The following video modes are defined on this version of the Vector Video card:
Mode 0: 128x128 resolution, 2 memory transfers per screen update
Mode 1: 32767x32767 resolution, 3 memory transfers per screen update
Mode 2: Text mode, <>x<> characters.
Mode 3: High resolution text mode, <>x<> characters.

2.2 Data encoding
The data for the display is encoded in the video ram in different ways depending on the video mode selected
    1. Mode 0
The data for the display is encoded as follows:
0	1	2	3	4	5	6	7	8	9	A	B	C	D	E	F
End	Beam	X0	X1	X2	X3	X4	X5	X6	Y0	Y1	Y2	Y3	Y4	Y5	Y6

        First write Second write
- End: Denotes the end of the memory, cells after this point are not to be drawn and the circuitry starts drawing at address 0 again.
- Beam: Indicates if the beam is to be drawn while moving to the location in memory
- X0..X6: represent the X coordinate of the vector on the screen
- Y0..Y6: represent the Y coordinate of the vector on the screen
Entering the data into the memory is done the same way as it is encoded.

    1. Mode 1
The data for the display is encoded as follows:
0	1	2	3	4	5	6	7	8	9	A	B	C	D	E	F
End	Beam	X0	X1	X2	X3	X4	X5	X6	Y0	Y1	Y2	Y3	Y4	Y5	Y6

        First write Second write
10	11	12	13	14	15	16	17
X7	X8	X9	XA	Y7	Y8	Y9	YA

        Third write
- End: Denotes the end of the memory, cells after this point are not to be drawn and the circuitry starts drawing at address 0 again.
- Beam: Indicates if the beam is to be drawn while moving to the location in memory
- X0..XA: represent the X coordinate of the vector on the screen
- Y0..YA: represent the Y coordinate of the vector on the screen
Entering the data into the memory is done the same way as it is encoded.

    1. Mode 3&4
The data for the display is encoded as follows:
0	1	2	3	4	5	6	7	8	9	A	B	C	D	E	F
End	Beam	X0	X1	X2	X3	X4	X5	X6	Y0	Y1	Y2	Y3	Y4	Y5	Y6

        First write Second write
10	11	12	13	14	15	16	17
X7	X8	X9	XA	Y7	Y8	Y9	YA

        Third write
- End: Denotes the end of the memory, cells after this point are not to be drawn and the circuitry starts drawing at address 0 again.
- Beam: Indicates if the beam is to be drawn while moving to the location in memory
- X0..XA: represent the X coordinate of the vector on the screen
- Y0..YA: represent the Y coordinate of the vector on the screen
Entering the data into the memory in text mode is done in a different way than the other modes:
0	1	2	3	4	5	6	7
D0	D1	D2	D3	D4	D5	D6	D7

        First write
## 3. Hardware solution
  1. RAM
The module will approximately use 4 kilobytes of RAM, this should be plenty for most applications.
3.1.1 RAM access
RAM access will be regulated by a Memory Access Controller. When data is written to the card, it first gets latched into the input buffer. It cannot be latched again until the card reports that the latch is empty. This signal is passed to the Pandora bus through the READY sense line to alert the processor of its state if it's listening. The latch gets cleared and the data gets written into the RAM on even cycles of the clock signal, this signal is multiplied on board using a delayed XOR to double the system's clock, making it possible to write to RAM every CPU cycle and simultaneously draw the screen.
Not only data , but also the memory location is latched into the card, so that on the writing cycle of the RAM, the circuitry will know to which location the data is to be written.
3.2 DAC
The DAC will be 12 bits wide to make full use of all of the 12 bits of information stored in RAM. The DAC will consist of a resistor ladder with appropriate values. The signal into the DAC is provided by a set of two latches, one set to get all the values from the RAM where they need to be, another to keep the correct values at the DAC until the next values have been loaded.
<TODO, offset signal with -2.5V>